## Slide 1: Intro to Hybrid Control Strategy
Lecture 11
MBDCP

## Slide 2: Need for an HVSC
A Hybrid Vehicle Supervisory Controller (HVSC) is needed to control the components in a hybrid powertrain when there are multiple torque sources
The objective of the HVSC is to minimize fuel consumption and energy consumption through balancing the SOC of the battery
There are different approaches to SOC management that are used throughout hybrids today
Notes: Mention coordination of multiple torque sources
Minimize fuel consumption/energy consumption not balance SOC

## Slide 3: Basic SOC Management
For the HVSC we will be designing, we will be implementing a simple PID controller coupled with a Genset command to turn on and off the engine and generator
The genset being turned on and off will be determined by the target SOC as the current SOC
This is thermostatic control if the power level of the genset remains constant
Notes: Not talk about thermostatic (only one operating power level) – engine/gen on/off control dictated by SOC

## Slide 4: Charge Balancing
In order to maintain a charge sustaining strategy, charge balance must be achieved
Charge balancing is when the initial SOC and final SOC are the same after a given drive cycle
To achieve charge balance, the net change in battery energy must be < 1% of the used fuel energy over a drive cycle
The initial SOC can be iterated in modeling in order to attain a charge balance

## Slide 5: Thermostatic Control
Max SOC
Min SOC
Initial SOC
Final SOC

## Slide 6: Simple vs. Complex
HVSC models can become vastly complex in nature because more complex strategies will attempt to achieve the most efficient path
Paths vary based on the power demand of the driver, as well as operating points of the engine and traction motor
Engine efficiency is a major factor because of how inefficient IC engines are. The more efficient operating points of an engine can be found using an efficiency map (typically at high torque, low speed)
Notes: prioritization

## Slide 7: Simple HVSC Design
In our model, the HVSC will operate based on a set target SOC versus the current target SOC. A PID controller with an output to genset power command will be used to regulate the SOC.
In addition to a PID, Stateflow will be used to turn the genset on and off based on the need to reach the desired SOC

## Slide 8: Overview of Stateflow
Stateflow is an addition to MATLAB that is primarily used for logic decisions that are based on input conditions
Stateflow has “states” that the model can be in, and depending on the state (which is based on the input conditions) the outputs will vary
The Stateflow model we will be using is very simple and easy to set up

## Slide 9: Stateflow Example: Genset Command
For our application we will be using Stateflow to determine the state of the Genset Command, or turning the engine/generator on and off
Genset ON
Genset OFF
Enter
Conditions to exit “Genset ON” and enter “Genset OFF”
Conditions to exit “Genset OFF” and enter “Genset ON”

## Slide 10: Complex HVSC
This is an extremely simplified version of an HVSC. For more information about HVSC’s, refer to OSU’s course on controller design:
Model Based Design: Supervisory Control & Fault Diagnosis