## Slide 1: Series PHEV Architecture Breakdown & Braking
Lecture 12
MBDCP

## Slide 2: Series PHEV Architecture
The next model we will generate will be of a series PHEV
This model will include the use of a genset to charge the battery as well as regenerative braking and the development of a simple HVSC to operate the vehicle
High
Voltage
Battery
Single
Speed
Trans
Traction Motor
DC/DC Converter
Grid Electricity In
Engine
Generator Motor
Fuel Tank
Fuel In
Accessory Load

## Slide 3
HVSC
Engine
Generator
Battery
P
DC/DC
Converter
Traction
Motor
Driveline
Glider
Driver
APP
Drive Cycle
Vehicle Speed
Losses
Losses
Losses
Losses
Losses
Losses
Brake
System
BPP
Friction Brake Force
Engine Power Command
Genset On/Off
Accessory Load
SOC
Post processing
Regen Brake Command
Rev 12/4/2012 DOrd
Power
Data Signal
Force
Series PHEV – Power Loss
Torque-Speed
Notes: Explain the architecture functionality – genset, regen brake, drive with tract motor, power node

## Slide 4: Key Notes for the Series
Discharging the battery implies a POSITIVE current while charging the battery implies a NEGATIVE current in our convention. This is not always the case!
The engine should have a minimum operating power limit to keep the engine from operating in poor regions of efficiency

## Slide 5: Braking System
In previous models, we have been modeling braking by having the driver model command a “brake force” to the driveline of the vehicle
To include regen braking in our system, we must use both friction brakes and regen braking to meet the total brake demand of the driver
The percentage of each braking force is dependent on a Regen Brake Fraction or RBF

## Slide 6: Braking System
We will use brake pedal position (BPP) to find the driver brake demand
The commanded brake force is broken down into two signals, the friction brake force and the regen brake force
These signals are routed to their respective systems (driveline and traction motor respectively) to account for the total demanded brake force

## Slide 7: Regen Braking
Regen braking commands a negative torque to the traction motor which slows the vehicle speed while sending energy to the battery
The motor model and driveline model are not efficiency models, so bidirectional flow is possible without modification to the models
Energy capture does have power losses associated with each component!