## Slide 1: Intro to DFMEA
Lecture 13
MBDCP

## Slide 2: What is DFMEA?
Design Failure Modes and Effects Analysis
Looks at different possible modes of failure for a part and documents the causes and actions associated with each failure
Each failure mode has several attributes that increase or decrease the final risk priority number or RPN
Includes ability to detect the failure, the severity of the failure, and the frequency of occurrence of the failure

## Slide 3: Example DFMEA
Item | Potential Failure Mode | Potential Effects of Failure | Severity | Potential Cause/ Mechanism of Failure | Occurrence | Current Design Controls Prevention | Current Design Controls Detection | Recommend Actions | Detection | RPN
Battery | High Temp | Battery could catch fire | 10 | Current drawn out of the battery at too high a rate for a period of time or inefficient cooling methods | 2 | Limitations on the current draw from the battery and a passive cooling system | Monitor the temperature of the battery using a sensor | Open battery contactors | 1 | 20

## Slide 4: DFMEA in Modeling
Modeling is used to validate DFMEA to assure that the model reacts appropriately if a fault does occur
Controllers in the vehicle have diagnostics that detect and act on faults
Faults can be inserted into models in order to test if the controllers act how they are designed to when a fault occurs

## Slide 5: More on Diagnostics
For more information about DFMEA and fault analysis, go to OSU’s course:
Model Based Design: Supervisory Control & Fault Diagnosis