## Slide 1: Longitudinal Vehicle Dynamics, Drive Cycles
MBDCP
Lecture 2

## Slide 2: Forces Resisting Motion
Several forces exist that oppose the motion of the vehicle:
  Rolling Resistance (Frr)
  Aerodynamic Drag (Faero)
  Grade Force (Fgr)
  Inertial Force (Fi)
These forces add together to equal the tractive effort (Ftr) of the vehicle, or:
Always show these forces on a diagram to establish signs!

## Slide 3: Rolling resistance from tires
Energy Dissipation due to Tire Deformation
Direction of Rotation
Direction of Travel

## Slide 4: Rolling Resistance Force (N)
  Where
  is coefficient for rolling resistance (unitless)
  m is vehicle mass (kg)
  g is gravitational constant (9.81 m/s2)
is dependent on the tire construction, road surface, age/tread, load, temp, inflation, etc.
Can be split between front and rear if the weight distribution is different

## Slide 5: Rolling Resistance models
  Is the simplest model = constant force
  More complex models have more terms, proportional to velocity, V2, etc.
See SAE Standard J2452: Stepwise Coastdown Methodology for Measuring Tire Rolling Resistance

## Slide 6: Aerodynamic Forces
  Where
  is air density (1.2 kg/m3)
  is frontal area of the vehicle (m2)
  is coefficient of drag (unitless)
  is vehicle velocity (m/s)
Forces are in Newtons, N (from kg-m/s2)
Note that Power (W) = FV, so P ~ V3

## Slide 7: Drag Coefficient and Frontal Area
The frontal area (Af) of the two vehicles shown is the same, however Vehicle B has a significantly smaller drag coefficient, thus will have a smaller aerodynamic drag force.
A
B
0.6
0.32

## Slide 8: Grade Force
Vehicle
Weight (mg)
Grade
(Fgrade)

## Slide 9: Inertial Force
  Usually most significant force acting on the vehicle, so mass is the most important vehicle property
  Use inertial mass to account for tire/wheel rotating inertia, usually

## Slide 10: Vehicle Glider
All these forces together sum to tractive effort
  Tractive effort is the force that drives the vehicle
  A vehicle dynamics model (or glider) uses these forces to obtain the vehicle speed, total energy consumption, as well as other numerous values for the vehicle, provided a drive cycle

## Slide 11: Alternative force balance
Solve for inertia/acceleration from tractive effort
  )
  Tractive effort comes from Driver Demand (and powertrain capability); may also be zero (coast) or negative (braking)
  A “Forward” model solves for vehicle acceleration and velocity from a commanded tractive effort at wheels

## Slide 12: Alternative road load form
EPA dynamometer tests use “Target ABC”s for road load, measured from vehicle coastdown
The EPA road load equation is:
where F is in units of pound-force [lbf] and V is the vehicle velocity in miles per hour [mph], thus the units for the coefficients are:
              A [lbf]
              B [lbf/mph]
              C [lbf/mph2]

## Slide 13: Drive Cycles or Schedules
Drive cycles are measured or generated velocity vs time profiles used to test or model vehicles
Each drive cycle contains different characteristics in order to mimic different driving scenarios in real life
In particular we are interested in the UDDS, HwFET, and US06 drive cycles

## Slide 14: Typical mode, or “Hill”

## Slide 15: Urban Dynamometer Drive Schedule (UDDS)
Drive cycle for relatively low speeds and fairly frequent braking and stopping

## Slide 16: Highway Fuel Economy Test (HWFET)
Drive cycle related to the driving patterns on a highway (high speed, little stopping)

## Slide 17: US06
Most aggressive drive cycle used to test “real world” driving of vehicles (heavy acceleration, braking, top speed of 80 mph)

## Slide 18: Driver Model
Using these drive cycles, a driver model will be created to attempt to match the velocity profiles by varying a certain value
Our driver model will consist of a PID controller
Can be varied to mimic different types of drivers (racing, typical)
Allows to see if the vehicle was able to match the drive cycle performance-wise

## Slide 19: Trace Misses
If the driver is not able to match the input drive cycle by > 2 mph, it is noted as a trace miss.
Trace misses indicate where the vehicle components could not match the acceleration/deceleration of a drive cycle (engine cannot produce enough power for example), or Driver model may not be responsive enough!