## Slide 1
Power Loss Models for Vehicle Powertrain Components
MBDCP
Lecture 3

## Slide 2: Vehicle Powertrain Component Models
To begin, we want to understand losses in the system; losses determine vehicle energy consumption and component heat generation
Detailed models are usually specific to a particular component and size/power; often hard to find and understand the required data
So start with a very basic and simple Power Loss model that still has all the needed behavior

## Slide 3: Power Loss model
A Power Loss model can be fit to and used for most any component with reasonable estimates and accuracy (model fidelity)
Need to look at an average operating power line
Later we will develop and use models based on torque and speed – for more details
Total energy can be integrated
Average losses = heat rejection rates
Energy/power balance: Input = Output + Losses

## Slide 4
Traction
Motor
Pin
Ploss
Pout
Power balance (or conservation of energy)
In this case, Pout is being commanded (driver demand, for example), so Ploss is a function of Pout
Power Loss Model

## Slide 5
Generator
Pin
Ploss
Pout
In this case, Pin is being commanded (from connection to an engine, for example), so Ploss is a function of Pin
Note: the constants are different from the above case
Alternate form of Power Loss Model

## Slide 6
HVSC
Engine
Generator
Battery
P
DC/DC
Converter
Traction
Motor
Driveline
Glider
Driver
APP
Drive Cycle
Vehicle Speed
Losses
Losses
Losses
Losses
Losses
Losses
Brake
System
BPP
Friction Brake Force
Engine Power Command
Genset On/Off
Accessory Load
SOC
Post processing
Regen Brake Command
Rev 12/4/2012 DOrd
Power
Data Signal
Force
Series PHEV – Power Loss

## Slide 7: Efficiency vs Losses
Losses are always positive (check your model!)
Efficiency can be defined as Output/Input, but this definition depends on power flow direction
The Power Loss model works for positive or negative power flow (regenerative braking using the motor, for example)
Use Loss models (or maps) for specific components, rather than Efficiency maps