## Slide 1: Overview of MATLAB driven Simulink Models
Lecture 4
MBDCP

## Slide 2: MATLAB driven Simulink
In this course we will be using MATLAB/Simulink to generate and simulate models
A MATLAB driven Simulink model uses a MATLAB m-file to simulate models in Simulink
MATLAB primarily used to define variables and postprocessing
Data can be passed between MATLAB and Simulink

## Slide 3: Setup
There are a couple of things that need to be setup in order to properly run a model
You must define your input and output variables in Simulink
Identifying simulation time and limiting step sizes
Understanding the data import and export!

## Slide 4: Setting Up Configuration Parameters
Under the “simulation” tab in Simulink there are configuration parameters
In this tab is where you can modify how Simulink runs, such as the solver it uses or how it imports and exports data

## Slide 5: Editing the Solver
The only things you should modify in this tab are the min/max step sizes, and the simulation stop time
In most cases the step sizes can be left on “auto”
Change the simulation stop time to a variable that can be defined in MATLAB

## Slide 6: Data Import/Export
The Data Import/Export tab handles how Simulink takes in and puts out data
You can change the names of the variables that are used for input and output, as well as the simulation time vector (defaults are u, yout, and tout respectively)
Uncheck the “Limit data points to last:” in order to prevent losing data

## Slide 7: Defining variables in MATLAB
Using the variables we put into Simulink previously, we can now declare their values in MATLAB
Variables are case sensitive, the variables must match each other exactly
Data being imported into Simulink must be an array with a time column associated with the signal values

## Slide 8: Data Exported from Simulink
The data that is put into “out” ports in Simulink will be stored in the matrix “yout”
For each data signal passed out of Simulink, a separate column is generated and stored. The order the columns hold the data corresponds to the number associated with the exported signal in Simulink
The “tout” array contains the simulation time, or steps taken by the model. This is particularly useful for plotting data generated by the model