## Slide 1: Vehicle Powertrain Architectures
Lecture 6
MBDCP

## Slide 2: Architectures for Vehicles
We will model several different powertrain architectures, including conventional vehicles, battery electric vehicles, and hybrid vehicles
Progressing from the simplest powertrain architectures to the more complex
The architectures can build off of each other and can be used to draw advantages and disadvantages of each architecture

## Slide 3: Powertrain Architectures
Conventional Vehicle
  What most of you drive!
  Uses fuel as energy input
  Least efficient architecture due to the exclusive use of engine
  Unidirectional Power Flow
  Powertrain Includes:
    Engine
    Driveline
Multi Speed Trans
Engine
Fuel Tank
Fuel In

## Slide 4: Powertrain Architectures
Battery Electric Vehicle (BEV)
  Pure Electric Vehicle
  High efficiency
  Bidirectional Power Flow using regen braking
  Powertrain includes:
    Traction Motor
    Single Speed Transmission
    Battery
    DC/DC Converter
High
Voltage
Battery
Single
Speed
Trans
Traction Motor
DC/DC Converter
Accessory Load
Grid Electricity In

## Slide 5: Powertrain Architectures
Series Hybrid
  Bidirectional Power Flow
  Only electric motor can put torque to the wheels
  Efficient at lower speeds, such as city driving, but inefficient at highway speeds
  Powertrain includes:
    Engine
    Transmission
    Battery
    DC/DC Converter
    Traction Motor
    Generator Motor
High
Voltage
Battery
Single
Speed
Trans
Traction Motor
DC/DC Converter
Grid Electricity In
Engine
Generator Motor
Fuel Tank
Fuel In
Accessory Load

## Slide 6: Powertrain Architectures
Parallel Hybrid
  Engine and Motor can both put torque to the wheels
  More efficient than the series at highway speeds
  Bidirectional Power Flow
  Optional to put generator between engine and transmission
  Powertrain includes:
    Engine
    Traction Motor
    Battery
    DC/DC Converter
    Multi-in Transmission (in some cases)
High
Voltage
Battery
Traction Motor
DC/DC Converter
Grid Electricity In
Fuel Tank
Fuel In
Accessory Load
Multi Input Trans
Engine