## Slide 1: Power Loss Component Example in Simulink
Lecture 8 (Simulink Example)
MBDCP

## Slide 2: Power Loss Example: Pout Known
In this example we will demonstrate how to construct a power loss model where Pout is known
This orientation of a power loss model can be used to represent components such as an engine or traction motor
The model being demonstrated (engine model) takes in accelerator pedal position as a percentage (%) and outputs engine power

## Slide 3: Engine Preview
Engine Model: Generates power based on APP from the driver model. Calculates Ploss(Pout) and Pin(Pout) to find energy/fuel consumption

## Slide 4: Engine Preview
The engine power out that is used to “power” the model (EngPwrOut(W)) is calculated as a percentage of the engine max power
In order to calculate the total Pout of the engine, the 12V accessory load must be added to the power leaving the engine

## Slide 5: Engine Preview
Using the calculated Pout, the power loss of the engine can be calculated using the provided C0, C1, and C2 values. This equation will appear in a lot of models we use in this course so it’s important to be familiar with it! Keep in mind units should be in Watts.

## Slide 6: Engine Preview
Using the previously attained values of Pout and Ploss, Pin can be calculated. Using an integrator block, the total energy being put into the engine (Ein) in units of Joules can be found. From this, useful values such as the fuel consumption can be found from unit conversion
Ploss can also be integrated in order to find the energy consumed by losses for the drive cycle in Joules