## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 1.2
How Do Batteries Work?
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: The Basic Battery Cell
Electrodes: Electronic conductors with different potentials [1].
Separator: Material that allows ions to pass through it, but not electrons [2].
Electrolyte: Ionic conductor to allow the movement of ions [1].
Current Collectors: Provide a path for electrons to flow through to the external circuit [2].

## Slide 4: Anode and Cathode Definitions
Anode: The electrode where negative ions flow towards, building up a negative charge [2].
Cathode: The electrode where the positive ions flow towards, building up a positive charge [2].
The charges of the anode and cathode create a cell voltage v(t) [2].

## Slide 5: Discharge
Negative electrode = Anode [2].
Positive electrode = Cathode [2].
Positive ions flow through electrolyte and separator from the anode to cathode [2].
Negative ions flow in the opposite direction [2].
A cell voltage v(t) is created due to this difference.
Electrons flow through an external circuit from the anode to the cathode. Positive current flows in the opposite direction of electrons as a convention [2].

## Slide 6: Charge
Negative electrode = Cathode [2].
Positive electrode = Anode [2].
Ions and electrons flow in opposite direction as compared to discharge [2].
The negative electrode has a higher potential, which allows the storage of energy.

## Slide 7: Reasons for Ion Movement
Diffusion
  Electrolyte will have a concentration gradient due to ions being produced from electrodes [2].
  Ions will flow to balance the concentration [2].
Migration
  An electric field is present, and moves positive ions to the cathode, and negative ions to the anode [1].
Convection:
  Bulk fluid motion, which mixes the electrolyte solution [1].

## Slide 8: References
[1] J.S. Newman and K.E. Thomas-Alyea. Electrochemical Systems. 3rd ed. Hoboken, NJ: J. Wiley, 2004.
[2] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.