## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 1.3
Different Battery Chemistries
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: Battery Chemistries involving HEVs
Three important battery chemistries when discussing hybrid electric vehicles
  Lead-acid (Pb-acid)
  Nickel-metal hydride (Ni-MH)
  Lithium-ion (Li-ion)
A cylindrical lithium-ion battery.

## Slide 4: Lead-acid Batteries: Materials and Reactions
Electrolyte
  Sulfuric acid (H2SO4)with water (H2O) [1].
  In water, the acid disassociates into H+ and HSO4- ions [1].
  Materials are porous to allow electrolyte to fill it [1].
Negative Electrode
  Made of lead (Pb) [1].
  During discharge, the reaction is a reduction reaction [1]:
Positive Electrode
  Made of lead (Pb), coated with a layer of lead oxide (PbO2) [1].
  During discharge, the reaction is an oxidation reaction [1]:
Charging the battery reverses the direction of these equations in each electrode.

## Slide 5: Lead-Acid Batteries: Benefits and Drawbacks
Tend to have high round trip efficiencies [1].
Old technology, so understood well and commonplace in most vehicles.
Theoretical voltage of 1.9V [1].
Energy density of 70 Wh/L [1].
Energy efficiency of ~70% [1].
Power density of 450 W/L [1].
Major factors involved in battery life [1]:
  Positive electrode can become corroded over time which leads to an increase in resistance.
  Gas is generated in overcharge, which will require the release of water to compensate.
  Sulfation can create PbSO4 crystals, and potentially decrease battery capacity.
  Mechanical stresses can cause material degradation.
  Dendritic lead may cause a short circuit by filling pores of separator.

## Slide 6: Nickel-Metal Hydride Batteries: Materials and Reactions
Electrolyte
  Potassium Hydroxide (KOH) or another alkaline solution [1]-[2].
Negative Electrode
  Made of hydrogen absorbing nickel alloys (MH) [1].
  During discharge, the reaction is a reduction reaction [1]:
Positive Electrode
  Made of nickel hydroxide (Ni(OH)2) [1].
  During discharge, the reaction is an oxidation reaction [1]:
Charging the battery reverses the direction of these equations in each electrode.

## Slide 7: Nickel-Metal Hydride Batteries: Benefits and Drawbacks
Tend to have higher performance than lead-acid batteries, but are more expensive [1].
Self-discharge much faster than most batteries chemistries [1].
Theoretical voltage of 1.35V [1].
Energy density of 240 Wh/L [1].
Energy efficiency of ~70% [1].
Power density of 300+ W/L [1].
Major factors involved in battery life [1]:
  Hydrolysis: loss of water increases internal resistance.
  Corrosion: speeds up loss of water, reduces active material in negative electrode.
  Decrepitation: stresses lead to loss of active material.

## Slide 8: Lithium-Ion Batteries: Materials and Reactions
Electrolyte
  Liquid or gel-polymer [1].
Separator is a micro porous, polymer film that allows ions to diffuse through it [1].
Negative Electrode
  Made of a lithiated carbon () [1].
  During discharge, the reaction is a reduction reaction [1]:
Positive Electrode
  Made of a lithium metal oxide () [1].
  During discharge, the reaction is an oxidation reaction [1]:
Charging the battery reverses the direction of these equations in each electrode.

## Slide 9: Lithium-Ion Batteries: Positive Electrode Chemistries
The lithium metal oxide () in the positive electrode can incorporate different metals.
Using Cobalt (LiCoO2):
  Easily prepared, and thus commonly used [3].
  High cost [3].
  Relatively toxic [3].
  Stability is not very high [4].
Using Manganese (LiMn2O4):
  Lower cost than LiCoO2 [4].
  Safer than LiCoO2 [4].
  Less capacity than LiCoO2 [4].
  Capacity loss after cycling is great at first, but tapers off [4].
Using Iron (LiFePO4):
  Low conductivity and voltage [4].
  Does not lose much capacity after cycling [4].

## Slide 10: Lithium-Ion Batteries: Benefits and Drawbacks
Have higher energy and power density when compared to most battery chemistries [1].
Self-discharge is very slow [1].
Very high initial cost [1].
Theoretical voltage of 4.1V [1].
Energy density of 400 Wh/L [1].
Energy efficiency of 80% [1].
Power density of 800+ W/L [1].
Major factors involved in battery life:
  Solid/Electrolyte Interface (SEI) layer growth: a necessary layer for conducting ions that consumes Li+, but as a result removes active material. If disconnected from electrode, resistance increases further [2].
  Lithium can be corroded, which results in a loss of active material [1].
  Lithium plating, generally caused at low temperatures or voltages, causes a loss in lithium [1].

## Slide 11: References
[1] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.
[2] J.S. Newman and K.E. Thomas-Alyea. Electrochemical Systems. 3rd ed. Hoboken, NJ: J. Wiley, 2004.
[3] B. Ammundsen and J. Paulsen, “Novel Lithium-Ion Cathode Materials Based on Layered Manganese Oxides,” Advanced Materials, vol. 13, no. 12–13, pp. 943–956, Jul. 2001.
[4] J. W. Fergus, “Recent developments in cathode materials for lithium ion batteries,” Journal of Power Sources, vol. 195, no. 4, pp. 939–954, Feb. 2010.