## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 2.1
Modeling of Dynamical Systems
Mohammad Ghanaatpishe
Donald Docimo
Hosam Fathy

## Slide 3: Dynamical Systems
In control engineering, we use mathematical formalizations to model the behavior of a physical system.
Such a mathematical relation predicts the behavior (outputs) of the physical system under consideration, in terms of the parameters (inputs) that could affect its state.
  Example: Ohm’s Law
I

## Slide 4: Battery Models
Battery Model
  Typical Inputs: Current, Ambient temperature
  Typical Outputs: Voltage, State of Charge, State of Health, Electrolyte concentration, etc.
Battery Model
Inputs
Outputs

## Slide 5: System Modeling
A critical step in modeling process is to study different characteristics and dynamics of the system under consideration.
A series of experiment is designed to obtain the response of the system to different inputs.

## Slide 6: System Modeling
In the validation stage, we make sure that the predicted output of the model agrees with the experimental results within an acceptable tolerance.
Input Current
Terminal Voltage
Battery Cell

## Slide 7: Frequency Response
For many dynamical systems, rate of change of the inputs greatly affects the response.
Using sinusoidal inputs, we can study the frequency-dependence of the response of the system.

## Slide 8: Frequency Response
The response of a dynamical system to a sinusoidal input is usually sinusoidal with a potentially different phase and amplitude.

## Slide 9: Frequency Response
A common practice to summarize the frequency response is to construct a vector of magnitude of the amplitude ratio, and angle of the phase difference of the response for every frequency.
Drawing these vectors in a coordinate system with the origin as the starting put and passing a curve through all the vector tips, we obtain what is called the Nyquist diagram of the system.
|

## Slide 10: Frequency Response
Example 1: Resistors
  Input: Current, I
  Output: Voltage, V
I

## Slide 11: Frequency Response
Example 2: Capacitor
  Input: Current, I
  Output: Voltage, V
I

## Slide 12: Frequency Response
Example 3: Inductor
  Input: Current, I
  Output: Voltage, V
I

## Slide 13: Frequency Response
Example 4: Parallel capacitor and resistor
  Input: Current, I
  Output: Voltage, V
  After a bit of computation, we obtain that the Nyquist plot of this pair forms a semicircle.
e(Z)
-(Z)

## Slide 14: Frequency Response
The frequency response of battery systems have been widely studied through the Electrochemistry Impedance Spectroscopy (EIS) technique.[2]
Electrochemists use a slightly different version of Nyquist plots, where the Negative vertical axis is directed upward. [1]
Schematic EIS plot of a cell

## Slide 15: References
[1] C. Rahn and C.Y. Wang, “Battery Systems Engineering,” Chichester: John Wiley & Sons, 2013.
[2] A. Jossen, “Fundamentals of battery dynamics,” Journal of Power Sources 154, pp. 530-538, 2006.