## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 2.3
Salient Dynamics of Batteries
Mohammad Ghanaatpishe
Donald Docimo
Hosam Fathy

## Slide 3: Charge storage
  Batteries mainly show capacitance properties.[1]
  SOC is used to denote the amount of charge of a battery.
  Fully charged : 100% SOC, Fully depleted : 0 % SOC
+
_
100%
0%
SOC
Capacitance
Inductance

## Slide 4: Charge storage
  There are two ways to model the storage characteristic of a cell:
  Using a capacitor.
  Using a SOC-dependent voltage source along with the charge/discharge dynamic.
  ,
  is the capacity of the cell.[1]

## Slide 5: Internal Resistance
  Internal elements of the cell resist the flow of electrons.
  Includes the resistances of current collectors, active materials, electrolyte and separator.[4]
  The intersection of the EIS plot with the horizontal axis shows the total ohmic resistance.[4]
Rs

## Slide 6: Internal Resistance
  We model this by an ohmic resistor.
  As expected, a resistor in series with our electrical potential source can model these losses.
  Experiments show that in the middle range of the SOC this resistance is fairly constant.

## Slide 7: Self-discharge
A phenomenon in which internal chemical reactions reduce the stored charge of the battery without any connection between the electrodes.
It is a chemical reaction and tends to occur more quickly at higher temperatures.

## Slide 8: Self-discharge
Due to the existence of this parasitic branch some part of the total current entering battery is lost in a nonreversible reaction.[3]
It is modeled by using a typically large resistor in parallel with the electrical potential source.

## Slide 9: Mass transport effects
Ions transport in a battery by diffusion. Since diffusion causes concentration of ions at the location of charge transfer it produces over-potential.[2]
Diffusion has the dominant effect in the impedance spectrum of the cell at low frequencies (<1 Hz) and makes the linear section of the EIS plot.[2]
Mass Transport Effects

## Slide 10: Mass transport effects
we need an infinite number of resistors and capacitors placed in the below configuration to model the impedance induced by mass transport in a diffusion layer.[1], [2]
The impedance plot for this configuration gives a constant phase of 45˚ for the entire frequency range.[1], [2]
An element that describes this characteristic is called Warburg element.[1], [2]
Warburg Element

## Slide 11: Double layer and charge transfer effects
The solid/electrolyte interface (SEI) resists the charge transfer and creates an over-potential. [2]
A charge zone is formed on the SEI layer and since this behavior resembles a capacitor it is called double layer capacitance.[2]
These effects govern the response of the system at the middle range frequencies (1Hz-1KHz) and make the semicircular section of the EIS plot.[2]
SEI Layer Effects

## Slide 12: Double layer and charge transfer effects
A resistor and a capacitor in parallel models the over-potential at SEI layer.
As we saw in Example 4, the impedance spectrum plot for a parallel RC pair forms an exact semi-circle.
e(Z)
-(Z)

## Slide 13: Electric and magnetic effects
At very high frequencies (>1KHz), the inductance of metallic elements in the cell and wires makes the EIS plot drop vertically.[2]
Also, as the frequency increases the current passing through an conductor tends to flow more near the surface. This phenomenon is called the Skin effect.[2]

## Slide 14: Electric and magnetic effects
The skin effect decreases the useable cross-section area of the current collector and, hence, increases the total resistance of the cell.[2]
It shifts the tip of the high frequency section of the curve to the right.
Skin Effect
Inductance Effects

## Slide 15: Electric and magnetic effects
The inductance effects can be modeled using an inductor.
The skin effect is basically a resistor whose resistance increases with frequency.
Putting these two elements in series, we model the high-frequency dynamic effects of a cell.

## Slide 16: Ageing Effects
As a battery cycles its performance weakens.
State of Health (SOH) is used to quantify the age of batteries. It may be defined based on many different parameters.
Ageing, in general, increases the internal resistance of the cell.[2]

## Slide 17: Ageing Effects
Building an equivalent model that takes the changes of SOH into account won’t be an easy task to accomplish.
An easier way to do this, is to repeat the parameter identification process for our circuit model and update its elements with the results once in a while.

## Slide 18: SOC-variation Effects
EIS plots are obtained for constant SOCs.
Changes in the state of the charge of the cell mainly influences the mass transport effects.[2]
The high-frequency section of EIS plot is not much sensitive to SOC changes.[2], [4]
Schematic EIS plot of a cell at two different SOCs.

## Slide 19: SOC-variation Effects
To capture SOC-variation effects on battery dynamics in our model, we could assume SOC-dependent impedances for the elements of our circuit model.
This is practical only if experimental data for our specific battery chemistry is available.
Below figures show such characteristic curves for an LiFePO4 battery.
Internal resistance variation with SOC
Open circuit voltage variations with SOC

## Slide 20: References
[1] C. Rahn and C.Y. Wang, “Battery Systems Engineering,” Chichester: John Wiley & Sons, 2013.
[2] A. Jossen, “Fundamentals of battery dynamics,” Journal of Power Sources 154, pp. 530-538, 2006.
[3] M. Ceraolo, “New dynamical models of lead-acid batteries,” IEEE Transactions on Power Systems, vol. 15, no. 4, pp. 1184–1190, 2000.
[4] D. Andrea, M. Meiler, K. Steiner, Ch. Wimmer, T. Soczka-Guth, D.U. Sauer, “Characterization of high-power lithium-ion batteries by electrochemical impedance spectroscopy. I. Experimental investigation,” Journal of Power Sources 196, pp. 5334–5341, 2011.