## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 2.4
Battery models with different fidelity levels
Mohammad Ghanaatpishe
Donald Docimo
Hosam Fathy

## Slide 3: Overall Circuit Model
Connecting the individual elements modeling each dynamic effect, we obtain the overall circuit model.

## Slide 4: Model Simplification Complexity VS. Fidelity
Our models are never an exact realization of the underlying physical phenomenon.
Increasing model complexity usually leads to improvement in accuracy.
A complex model, even if obtained, might not be applicable because of the computational or other costs.

## Slide 5: High Frequency Dynamic Effects
For most of battery applications (including HEVs), load frequencies are within DC to 10Hz range.[1]
Neglect the high frequency dynamics.

## Slide 6: Model Order Reduction
Number of energy storage elements in the circuit determines the order of the model.
Using only one or two pairs of RC’s significantly reduces the complexity of the model, while we are still capable of capturing the transient dynamics of the cell.

## Slide 7: SOC Range of Variation
To lengthen the battery life, SOC of the cell is maintained in the middle ranges specially in highly dynamic applications.[1]
Using average values for our circuit parameters within these ranges, we can further simplify our model.

## Slide 8: Common Equivalent Circuit Models
We can yet simplify our model based on its specific application.
These are the most common equivalent circuit battery models with different level of fidelities and complexities.

## Slide 9: References
[1] C. Rahn and C.Y. Wang, “Battery Systems Engineering,” Chichester: John Wiley & Sons, 2013.