## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 3.1
Battery Packs and Cell Balancing
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: Battery Packs
The equivalent circuit model in Lesson 2 is for a single lithium-ion battery cell.
HEVs require larger currents and voltages that what a single battery cell can produce.
  Connecting cells in parallel will increase the current.[1]
  Connecting cells in series will increase the voltage.[1]

## Slide 4: Cell Balancing in a Battery Pack
All cells will have the same SOC (and voltage) in a battery pack if the pack is balanced. [1]
However, imbalance is common. Reasons for imbalance:
  No two cells are identical when produced.[1] Manufacturing volume differences and internal impedance differences. [2]
  Each cell will age differently.[1]
    Temperature is a major factor in aging.[1]
  Environmental effects:
    Temperature of the inner cells may not be the outer cells.[1]
  Loads not applied uniformly to all cells. This may even include the battery management system (that which controls the battery) itself.[1]

## Slide 5: Issues Caused by Cell Imbalances
Overcharging
  Reduced capacity and degradation.[1]
  Damages active materials.[3]
  Lithium-ion battery should not be overcharged, usually is dangerous.[2]
The capacity may be dictated by the weaker cell.[1]

## Slide 6: Methods to Balance Cells (Outside of a Control Strategy)
Cells in parallel are automatically balanced (they output the same voltage).[1]
Heating/cooling of cells helps.[1]
Cells with similar attributes (capacity) are generally grouped together when building the battery pack.[1]
These methods will not fully eliminate imbalance.[1]

## Slide 7: Balancing Circuit Options
Various different types of methods for balancing that could involve[2]:
  Resistors
  Capacitors
  Transformers
  Converters
Lesson 3 reviews two basic methods:
  Dissipative Shunting Resistor Method
  Single Switched Capacitor Method

## Slide 8: References
[1] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.
[2] J. Cao, N. Schofield, and A. Emadi, “Battery balancing methods: A comprehensive review,” 2008 IEEE Vehicle Power and Propulsion Conference, pp. 1–6, Sep. 2008.
[3] S. Moore and P. Schneider, “A review of cell equalization methods for lithium ion and lithium polymer battery systems,” SAE Publication, no. 724, 2001.