## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 3.2
Dissipative Shunting Resistor Method
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: Basics of Shunting Resistor Method
Method allows cells with higher voltage to release excess energy until the other cells are at the same voltage.[1]
General setup of dissipative shunting resistors for three cells in series.

## Slide 4: Cell Imbalance Detection
Voltage monitors are in parallel with each cell in the series.[1]
The controller is fed this information.

## Slide 5: Cell Imbalance Mitigation
A resistor is connected in parallel with each cell.[1]
The resistor is normally disconnected from the circuit through an open switch.

## Slide 6: Cell Imbalance Mitigation
In the figure below, the middle cell has a higher voltage than the other two cells.
The controller receives this information via the voltage monitor, and closes the switch for the second resistor.[1]

## Slide 7: Cell Imbalance Mitigation
With the connection made, the battery will dissipate heat through the resistor.[1]

## Slide 8: Cell Imbalance Mitigation
When the voltage monitor indicates that the middle cell has equal voltage to the other cells, the controller opens the switch.[1]

## Slide 9: Benefits and Drawbacks
Very easy to design and implement.[1]
No need for complex control.[1]
Generally the cheapest method.[2]
High energy losses.[2]
Can create a significant increase in battery temperature and other thermal management issues.[2]

## Slide 10: References
[1] J. Cao, N. Schofield, and A. Emadi, “Battery balancing methods: A comprehensive review,” 2008 IEEE Vehicle Power and Propulsion Conference, pp. 1–6, Sep. 2008.
[2] S. Moore and P. Schneider, “A review of cell equalization methods for lithium ion and lithium polymer battery systems,” SAE Publication, no. 724, 2001.