## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 3.3
Single Switched Capacitor Method
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: Basics of Single Switched Capacitor Method
Also referred to as the flying capacitor method.[1]
Method uses a single capacitor to transfer charges from higher voltage cells to lower voltage cells.[2]
  Note that there is a resistance in series with the capacitor. This resistance is due to the physical connectors.[3]

## Slide 4: Cell Imbalance Detection
No monitors are used for the most basic setups.[2]
Switches connect capacitor in parallel to each cell. [1]
Capacitor gains and loses charge quickly at first, so the switches flip quickly to take advantage of this (sometimes 5 kHz or 10 kHz).[3]

## Slide 5: Cell Imbalance Mitigation
Capacitor connected in parallel to the first cell.
The first cell has a higher voltage than the capacitor, and thus the capacitor takes some charge from the cell in an attempt to correct this.

## Slide 6: Cell Imbalance Mitigation
Capacitor is now in parallel with cell 2.
For this example, the voltages are the same in both the capacitor and this cell, so no charge is exchanged.

## Slide 7: Cell Imbalance Mitigation
Capacitor is now parallel with the third cell.
As the voltage of the capacitor is higher than the voltage of this cell, the cell takes some charge from the capacitor.

## Slide 8: Cell Imbalance Mitigation
The cycle of switching through each cell continues constantly.
When the voltages of the capacitor and the cells are all equal, the system is balanced.

## Slide 9: Benefits and Drawbacks
Only control needed is for the switching sequence.[1]
  No need for intelligent control.[2]
Can be improved to switch only between highest and lowest voltage cells, but would require voltage monitors and intelligent control.[2]
  Faster but more complicated and costly.

## Slide 10: References
[1] S. Moore and P. Schneider, “A review of cell equalization methods for lithium ion and lithium polymer battery systems,” SAE Publication, no. 724, 2001.
[2] J. Cao, N. Schofield, and A. Emadi, “Battery balancing methods: A comprehensive review,” 2008 IEEE Vehicle Power and Propulsion Conference, pp. 1–6, Sep. 2008.
[3] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.