## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 4.1
Battery Safety Concerns
Mohammad Ghanaatpishe
Donald Docimo
Hosam Fathy

## Slide 3: DFMEA
Design Failure Modes and Effects Analysis (DFMEA) is an essential part of product design and qualification process.[2]
It is a design review process to identify possible design failure scenarios related to the main functions of the product, determine the potential causes, and the risk associated with each of those failure modes.
The result is, then, followed by an action plan to design out the high-risk potential failure modes and repetition of the risk assessment process for the modified design plan.[2]

## Slide 4: DFMEA
In DFMEA, failures are prioritized according to their
  severity of consequences
  frequency of occurrence
  ease of Detection
  each ranked in a 1-10 scale.[2]
The overall risk of a failure mode is, then, quantified using Risk Priority Number (RPN) obtained by multiplying the three numbers assigned together.
The failure modes with the highest scores should be addressed through product redesign.
RPN = S × O × D.

## Slide 5: Battery Safety Concerns
Batteries have the potential to be dangerous if they are not carefully designed or if they are abused.
For a fully charged Li-ion cell modeled in Lesson 2:
The electrical energy density of a Li-ion cell is roughly 15% of that of common explosives such as TNT![1]

## Slide 6: Battery Safety Concerns
There are many possible scenarios in which a battery cell could fail.
The most important events we need to protect our cell from are:
  Over voltage
  Under voltage
  High/Low ambient temperature
  Excessive current during charge or discharge
  Physical abuse
  Short circuit

## Slide 7: DFMEA Chart for a Cell Safety Plan
Functions | Potential Failure Modes | Potential Effects | Severity | Occurrence | Detection | RPN
Terminal voltage of the cell is maintained within a specific operational range. | Over Voltage | Overheating/ Gassing | 6 | 6 | 3 | 108
 | Under Voltage | Anode dissolution | 5 | 6 | 3 | 90
The cell operates in its desirable temperature range. | Over Temperature | SEI layer break down | 6 | 4 | 3 | 72
 | Low Temperature | Lithium plating/ Capacity loss | 5 | 3 | 3 | 45
The amount of charge entering or leaving the cell is limited. | Over Current | Overheating/Lithium plating/Capacity loss | 6 | 6 | 4 | 144
The cell is protected against physical abuse. | Physical Damage | Short circuit/ Pressure build up | 9 | 2 | 5 | 90
Cell are made internally stable and safe. | Internal Short Circuit | Overheating/Thermal runaway | 9 | 2 | 9 | 162

## Slide 8: Cell Protection Plans
Battery Management System (BMS) monitors the key parameters of the pack including cell voltage, current and temperature. [1]
These data are used to trigger the safety protection devices such alarms, and switches to keep the battery operation within the design limits.

## Slide 9: Cell Protection Plans
Mitigation actions are taken when each of these events is detected:
Over Voltage
  Cut off the charger current.
Under Voltage
  Disconnect the pack from the load.
Over/Under Temperature
  Thermistors are circuit devices whose resistance varies with temperature.
  They can be used as temperature sensors or even thermal fuses.
Over Current
  FET switches are used to break the current path.[1]

## Slide 10: Cell Protection Plans
Not all of the threats to the battery safety can be mitigated externally.
Physical Abuse
  Robust Packaging
  Venting
  Current Interrupt Device (CID)
Internal Short Circuit
  It is detected by a sudden drop in voltage or increase in self-discharge current.[3]
  Not much can be done to protect the battery once it occurs.

## Slide 11: References
[1] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.
[2] Raytheon Six Sigma. (2007). Design Failure Modes and Effects Analysis (edition) [online]. Available: http://www.raytheon.com
[3] W. Cai, H. Wang, H. Maleki, J. Howard, E. Lara-Curzio, “Experimental simulation of internal short circuit in Li-ion and Li-ion-polymer cells”, Journal of power sources 196, pp. 7779– 7783, 2011.