## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 4.3
Mitigation of Short Circuiting Consequences
Mohammad Ghanaatpishe
Donald Docimo
Hosam Fathy

## Slide 3: Mitigation of Electric Shorts in Cells
The actions taken to decrease the probability or severity of occurrence of short circuits in a cell fall into two general categories:
  Cell design level
    Cell Chemistry
    Separator
  Pack design level
    Thermal management systems

## Slide 4: Cell Chemistry
Highly reactive materials are needed to provide the higher energy density cells, but they are likely to increase the risk of danger in case of cell failures.
There needs to be a compromise between power density and safety.
Replacement of Cobalt oxide by Manganese oxides as the cathode in Li-ion cells is an example of such a compromise.[4]

## Slide 5: Separators
Overheating might cause the separators to distort or melt which could lead to a short circuit between the electrodes.[3]
Various separators have been designed to avoid this problem, including
  Shutdown separators[3]
  Rigid separators[3]

## Slide 6: Thermal Management Systems
At the pack level, the only action possible to mitigate the consequences of short circuiting is to detect and isolate the defective cell of the pack.
To protect the cell, high rates of heat absorption is needed to keep the cell temperature below the on set of abuse reactions.[3]
At the same time, the heat absorbed should be dissipated in a way that does not affect the rest of the pack and, therefore, prevents the event propagation.

## Slide 7: Thermal Management Systems
Once the BMS detects a short circuit, there are different approaches to do battery thermal management using:
  Air[1]
  Liquid[1]
  Refrigerant[1]
  Phase-change material[1]

## Slide 8: Short Circuit Model for a Cell
Combining the circuit model obtained for a cell, and a simple energy balance equation we make a very simple model to simulate short circuits.

## Slide 9: Short Circuit Simulink Model
Parameter | Value
m | 70 g
Cp[2] | 700 J/(Kgk)
h | 10 w/(m^2k)
A | 50 cm^2
T_inf | 20
Rshort | 0.5
Parameter | Value
m | 70 g
Cp[2] | 700 J/(Kgk)
h | 10 w/(m^2k)
A | 50 cm^2
T_inf | 
Rshort | 
Cell Model
Thermal Model
The Simulink configuration shown here represents the combination of the equivalent circuit model and the energy balance equation.
The thermal response of a typical cell in presence of still air (no cooling mechanism) is simulated using the parameters given in the table.

## Slide 10: Short Circuit Simulation with No Cooling
SOC and cell temperature variations for a 2-minute simulation:

## Slide 11: Short Circuit Simulation with Water Cooling
The simulation results obtained by replacing the convective heat transfer coefficient of air by water as the cooling fluid:

## Slide 12: References
[1] C. Rahn, C.Y. Wang, “Battery Systems Engineering,” Chichester: John Wiley & Sons, 2013.
[2] A. A. Pesaran, Matthew Keyser, “ Thermal Characteristics of Selected EV and HEV Batteries”, Annual Battery Conference: Advances and Applications , Long Beach, CA, 2001.
[3] S. Santhanagopalan, P. Ramadass, J. Zhang, “Analysis of internal short-circuit in a lithium ion cell”, Journal of Power Sources 194, pp. 550–557, 2009.
[4] D. Belov, M. Yang, “Investigation of the kinetic mechanism in overcharge process for Li-ion battery”, Solid State Ionics 179, pp.1816–1821, 2008.