## Slide 1
AVTC Model Based Design Curriculum Development Project

## Slide 2
An Introduction to
Modeling an
Energy Storage System (ESS)
Lesson 5.1
State of Charge Estimation
Donald Docimo
Mohammad Ghanaatpishe
Hosam Fathy

## Slide 3: State of Charge (SOC)
It is a parameter that defines how much charge the battery is currently storing[1]
SOC is difficult to measure in practical applications[1]
  Hybrid electric vehicles do not have extreme operating ranges for SOC, but tend to have radical shifts within that range

## Slide 4: SOC Estimation
If SOC cannot be measured easily, it can be estimated
  Voltage, current, and temperature are measured for a battery[1]
  Using these measurements, estimates can be made for SOC
    This is related to cell balancing in lesson 3: there is a correlation between voltage and state of charge, as mentioned previously

## Slide 5: Defining Variables
Actual State of Charge | 
Estimated State of Charge | 
Initial State of Charge | 
Estimated Initial State of Charge | 
Capacity of Battery Cell | 
Internal Resistance of Battery Cell | 
Current Input | 
Output Voltage of Cell | 
Estimated Voltage | 
Actual State of Charge | 
Estimated State of Charge | 
Initial State of Charge | 
Estimated Initial State of Charge | 
Capacity of Battery Cell | 
Internal Resistance of Battery Cell | 
Current Input | 
Output Voltage of Cell | 
Estimated Voltage | 

## Slide 6: Simple SOC Estimation Methods: Current Counting[1]
Generally good for tracking the SOC if there is no noise in the input current.
If the initial SOC is not known, it is guessed, and that error won’t be corrected
Uses the equations:

## Slide 7: Simple SOC Estimation Methods: Voltage Lookup[1]
From Lesson 2, there is a relationship between open-circuit voltage (VOC) and SOC, that can be represented by VOC = f(SOC)
Use the output voltage V of the battery cell to determine the SOC.
Generally inaccurate without a filter.

## Slide 8: Feedback Observer[1]
Also called a feedback estimator or feedback filter.
Combines current counting and voltage lookup methods through the use of a gain

## Slide 9: References
[1] C. Rahn and C.Y. Wang. Battery Systems Engineering. Chichester: John Wiley & Sons, 2013.