## Slide 1: High-Tech Tools and Toys Lab at NU

## Slide 2: Hardware – Standard Agilent Test and Measurement Set
Power supply
Signal Generator
Multimeter
Oscilloscope

## Slide 3: HTT&TL Hardware
5-V stepper motor and IC controller
40 kHz ultrasound transducers
1 MHz ultrasound transducers and aquarium
X-Y positioner
Logitech videocam
Computer
  National Instruments PCI-6024E A/D card
  GPIB bus controller card

## Slide 4: HTT&TL Software
MATLAB Data Acquisition Toolbox
MATLAB Instrument Control Toolbox
National Instruments NI-DAQ A/D card controller software in C
MATLAB m-files
  one-step.m, cw.m, cc.m, readcell.m, setup_dio.m, direct.m, move.m, setup_tank.m, and pulseecho.m
C++ programs to download videocam using Python
  Binarize.h, Binarize.lib

## Slide 5: Part I High-Tech Tools and Toys Lab Ultrasound Imaging with MATLAB

## Slide 6: Lab 1: Measuring the Speed of Sound in Air
Two 45kHz transducers in air (“pitch/catch” configuration)
Delay time measured by digital oscilloscope – Distance by measuring tape on desk
5-10 x vs. t data points measured and plotted in Excel
Speed of sound in air determined by linear least square fit
Extension: measure amplitude vs. distance and fit to 1/x dependence [Energy= C*(Amplitude)2]

## Slide 7: HTT&TL Acoustic Instrumentation Package

## Slide 8: Measuring Speed of Sound in Air (EXCEL)

## Slide 9: Lab 2: MATLAB Programming – Control of Stepper Motor
Primitive programs provided
  onestep.m – moves stepper motor one step
  cc.m, cw.m – set direction
  readcell(dio, voltage) – reads photocell on dial
Student programs
  “for” and “while” loops
  “if – else” logic
Goal: measure stepper motor degrees per step

## Slide 10: First Programs: Control of Stepper Motor

## Slide 11: Lab 3: X-Y Positioner
Control x and y position of pen attached to positioner
Write MATLAB programs to:
  Write simple letters (H, T)
  Write more complicated letters (A, N, O)
  Draw raster pattern, recording the position of pen on a centimeter grid

## Slide 12: Lab 4: Speed of Sound in Water
1MHz ultrasound transducer attached to x-y positioner in aquarium
Transmitted and reflected pulses recorded on oscilloscope
Scope trace downloaded over GPIB bus
Program MATLAB to measure delay time from transmit pulse to reflected pulse
Program positioner to change distance to aquarium side and take data of x(i), t(i)
Plot x-t data points and least-squares fit to find slope=speed of sound in water

## Slide 13: Lab 5: Imaging Surface Shape
Goal: Use MATLAB program to image aluminum shape under opaque gelatin
Program x-y positioner to move 1 MHz transducer in raster pattern in aquarium
Download scope trace of V(t)
Process with MATLAB to find distance to target at each point
MATLAB 3D plot of distance vs. position shows shape of object

## Slide 14: Subsurface Shape in Opaque Gelatin

## Slide 15: Imaging a Subsurface Shape

## Slide 16: Subsurface Object Imaged

## Slide 17: Lab 6: Introduction to C++
Analyze “Speed of Sound in Air” data using C++ array process and linear regression formulas

## Slide 18: Part II High-Tech Toys and Tools Object-Sorting Labs
Create C++ program to identify color of video-cam output and actuate stepper motor to sort balls

## Slide 19: Lab 7: Digital Output
Call NI-DAQ program for digital output
  Measure DIO output with voltmeter
  Use 4 DIO 1-bit outputs to drive 4 LED’s
    Counting
    Bitwise AND and OR operations (& and |)
  Use DIO output to drive stepper motor
  Extention: Use Analog Input from photocell for position feedback

## Slide 20: Lab 8: Using Videocam to Recognize Colors
Use provided programs to:
  Capture image – image.Capture()
  Download pixels – image.GetPixels(A)
Distribute array A into 240 rows x 320 columns
Extract RGB values from 24-bit integer (bitwise AND)
Average RGB values and convert to HSV (Hue-Saturation-Value)
Use H (hue angle) to determine color of paper on clipboard
  Two colors (horizontal or vertical)
  Four colors
  Central color

## Slide 21: Lab 9: Sort Ping-Pong Balls by Color
Two-color sorting (Video 1)
  Recognize color of manually positioned ball
  Rotate right or left to receptacle tube 1 or 2
Four-color sorting (Video 2)
  Add linear actuator to hold up balls
  Recognize color of ball
  Rotate to appropriate receptacle tube (1-4)
  Activate linear actuator to drop ball
  Repeat for n balls

## Slide 22: C++ Control for Color-Sorting in HTT&TL
Notes: Replace with photo of other school

## Slide 23: High-Tech Tools and Toys Lab
Video 1: 2-color sorting (click image to start)

## Slide 24: High-Tech Tools and Toys Lab
Video 2: 4-color sorting (click image to start)