## Slide 1: Engineering Applications for Vectors & Matrices

## Slide 2: Solving Linear Equations using Arrays

## Slide 3: Solving Linear Equations
Many applications require solving systems of linear equations.
One method for solving linear equations is to write a matrix equation then apply some of the array operations discussed previously.
Procedure:
Write the equations in the form: Ax = b where A is a square matrix of equation coefficients, x is a vector of unknown variables, and b is a vector of constants.
Check det(A). If det(A) = 0, then there is no unique solution to the equations. If det(A) ≠ 0, invert matrix A and multiply both sides of the equation (on the left) by A-1.
The unknown variables, x, are given by x = A-1*b.

## Slide 4: Example: Solving Linear Equations
Solve the following system of linear equations:
x + 2y – 5z = -8
3x + y + 4z = 9
x + 2y – z = 0
Write matrix equation: 1 2 – 5 x -8
3 1 4 y = 9
1 2 –1 z 0
Does matrix A have an inverse?
*
Use MATLAB®: >> A = [1 2 -5; 3 1 4; 1 2 -1]; det (A)
ans =-20 So yes, A has an inverse!

## Slide 5: Example (continued)
Compute the inverse of matrix A (using MATLAB®) and then multiply both sides of equation (on left) by A-1.
>> inv(A)
ans = 0.4500 0.4000 -0.6500
-0.3500 -0.2000 0.9500
-0.2500 0 0.2500
x 0
y = 1
z 2
A-1*A = 1 0 0
0 1 0
0 0 1
MATLAB®
>> b = [-8; 9; 0];
>> inv(A)* b

## Slide 6: Example (continued)
Check Solution:
x + 2y – 5z = -8
3x + y + 4z = 9
x + 2y – z = 0
0 + 2(1) – 5(2) = -8
3(0) + (1) + 4(2) = 9
0 + 2(1) – 2 = 0 It Works!

## Slide 7: More Efficient Method: Left Divide
Previous Example with a Left Divide Operator:
>> A = [1 2 -5; 3 1 4; 1 2 -1]; det (A)
ans =-20
>> b = [-8; 9; 0];
>> A\b % Note the back slash here (not divide operator).
ans =
0.0000
1.0000
2.0000

## Slide 8: Mechanics
The behavior of physical objects
when subjected to forces

## Slide 9: Force: A Vector
Forces are specified using two quantities: the magnitude and the direction of the force.
In polar form, F = erFr + eθF θ
F = magnitude (Newtons, N or lbs)
θ = direction (degrees or rad)
In rectangular form F = iFx + jFy = Fx
Fy
F: magnitude
θ: direction
x
y
^
^
er,Fr
eθ,F θ
i,Fx
j,Fy

## Slide 10: Quick Review of Basic Trig
α
x
y
h
sin(α) = y/h
cos(α) = x/h
tan(α) = y/x
x2 + y2 = h2

## Slide 11: Force Conversions
Polar to Rectangular:
Fx = Fcos(θ) Force in x-direction
Fy = Fsin(θ) Force in y-direction
Rectangular to Polar:
F = √Fx2 + Fy2
θ = tan-1(Fy/Fx)
F
θ
x
y
Fx
Fy

## Slide 12: Computing Resultant Force
Numerical Solution:
Resolve each force into an x and y component (rectangular).
Sum all of the x components and all of the y components to get the x and y component of the resultant force.
Calculate the magnitude and direction of the resultant force from the x and y components.
F1 = 100∠50o N
F2 = 50∠-30o N
F3 = 30∠130o N

## Slide 13: Computing Resultant Force
F1 = 100cos(50) = 64.3 F2 = 50cos(-30) = 43.3 F3 = 30cos(130) = -19.3
100sin(50) 76.6 50sin(-30) -25 30sin(130) 23
Ftotal = F1 + F2 + F3 = 64.3 + 43.3 + -19.3 = 88.3
76.6 – 25 + 23 74.6
F1 = 100∠50o N
F2 = 50∠-30o N
F3 = 30∠130o N
64.3
76.6
43.3
-25.0
-19.3
23.0

## Slide 14: Computing Resultant Force
Magnitude = sqrt(88.32 + 74.62) = 115.6
Direction = atan(Fy/Fx) = 40.2o
Note: If Fx is negative, add 180o to the direction calculated using
MATLAB® or calculator.
F1 = 100∠50o
F2 = 50∠-30o N
F3 = 30∠130o N
F = 115∠40.2o N
74.6
88.3

## Slide 15: Computing Resultant Force Graphically
F1 = 100∠50o N
F2 = 50∠-30o N
F3 = 30∠130o N
Head to Tail Method

## Slide 16: Computing Resultant Force Graphically
F1 = 100∠50o
F2 = 50∠-30o N
F3 = 30∠130o N
Magnitude = 115.6
(measure length of vector)
Direction = 40.2o
(measure angle of vector)

## Slide 17: In MATLAB
>> F1 = [100*cosd(50); 100*sind(50)];
>> F2 = [30*cosd(130); 30*sind(130)];
>> F3 = [50*cosd(-30); 50*sind(-30)];
>> F = F1 + F2 + F3
F =
88.2964
74.5858
>> magnitude = sqrt(F(1)^2 + F(2)^2)
magnitude = 115.5824
>> if F(1) < 0 angleF = atand(F(2)/F(1))+180; else angleF = atand(F(2)/F(1)); end
>> angleF
angleF = 40.1885

## Slide 18: A Simple Statics Example
Weight = 50 lbs
A
C
B
A weight is suspended from two cables (AC and BC) which are secured at points A and B. Assuming the cables can support the weight and there is no motion, find the forces (tension) in the two cables.

## Slide 19: A Simple Statics Example
What do we know about the cable forces?
50 lbs
A
C
B
F1
F2
The two cables must provide 50 lbs of force in the positive
y- direction to counteract the force from the weight.
There should be no net force in the x-direction from the two cables.
Statics: ∑Fx = 0 ∑Fy = 0

## Slide 20: A Simple Statics Example
∑Fx = 0 F1x + F2x = 0
∑Fy = 0 F1y + F2y - 50 = 0
50 lbs
A
C
B
F1
F2
F2y
F1y
F2x
F1x
What other information do we need?

## Slide 21: A Simple Statics Example
θ1 = acos(7.5/10) = 41.4o
θ2 = acos(7/10) = 45.6o
50 lbs
A
C
B
F1
F2
F2y
F1y
F2x
F1x
7 in
10 in
7.5 in
10 in
θ1
θ2

## Slide 22: A Simple Statics Example
50 lbs
A
C
B
F1
F2
F2y
F1y
F2x
F1x
45.6o
41.4o
∑Fx = 0 F1x + F2x = 0 -F1cos(41.4o) + F2cos(45.6o) = 0
∑Fy = 0 F1y + F2y - 50 = 0 F1sin(41.4o) + F2sin(45.6o) - 50 = 0
∑Fx = 0 F1x + F2x = 0 F1cos(138.6o) + F2cos(45.6o) = 0
∑Fy = 0 F1y + F2y - 50 = 0 F1sin(138.6o) + F2sin(45.6o) - 50 = 0
OR

## Slide 23: A Simple Statics Example
∑Fx = 0 -F1cos(41.4o) + F2cos(45.6o) = 0
∑Fy = 0 F1sin(41.4o) + F2sin(45.6o) = 50
In Matrix Form:

## Slide 24: A Simple Statics Example
MATLAB SOLUTION:
>> A = [-cosd(41.4) cosd(45.6) ; sind(41.4) sind(45.6)] ;
>> b = [0; 50];
>> F = A\b
F =
35.03
37.56

## Slide 25: A Simple Statics Example
50 lbs
A
C
B
F1= 35.03 ∠138.6o lbs
(Tension)
F2= 37.56 ∠45.6o lbs
(Tension)
Always include units in your answers if possible!

## Slide 26: Circuit Analysis

## Slide 27: Basic Electrical Laws
Ohm’s Law: V = I * R
V = voltage (volts, V)
I = current (amps, A)
R = resistance (ohms, W)
Current - the flow rate of electrons in a circuit.
1A = 6.242⋅1018 e- /second
Voltage - the potential difference between two points in
a circuit.
Resistance - a measure of the opposition to the flow of
current in a circuit.
+
_
V
I
R

## Slide 28: Basic Electrical Laws (con’t)
Kirchoff’s Voltage Law: The sum of the voltage drops and rises around a loop is zero.
Kirchoff’s Current Law: Current flow into a node is equal to the current flow out of a node.
I1 = I2 + I3
I1
I3
I2

## Slide 29: Simple Circuit Example
Total Resistance, R=?
Current, I = ?
Voltage Drop Across Each Resistor?
Verify Kirchoff’s Voltage Law
I = 2 mA
VR1 = (2 mA)*(1 kW) = 2 V
VR2 = (2 mA)*(2 kW) = 4 V
VR3 = (2 mA)*(3kW) = 6 V
12V – 2V – 4V – 6V = 0 or 12V = 2V + 4V + 6V
+ 4V -
+ 2V -
+
6V
-
R = 1 kW + 2 kW + 3 kW = 6 kW
I = (12V) / (6000 W) = 0.002 A = 2 mA
+
_

## Slide 30: Mesh Analysis Circuit Example
I1
I2
I3
A student in a circuit class applies Kirchoff’s Voltage Law around each loop and derives the following equations:
+
+
_
_

## Slide 31: Mesh Analysis Example
Use the mesh equations to solve for the three loop currents.
Re-write the equations so the unknowns (currents) are on the left side and the constants are on the right side.

## Slide 32: Mesh Analysis Example
Now combine the three equations into matrix form:

## Slide 33: Mesh Analysis Example
Solve for currents using MATLAB®
>> R = [ 3.2 -2.2 0 ; -2.2 11.1 -3.3 ; 0 -3.3 8 ]; det (R)
ans =
210.5920
>> v = [9; 0; -6];
>> I = R\v
I =
3.1228
0.4513
-0.5638

## Slide 34: Mesh Analysis (continued)
I1 = 3.1228 mA
I2 = 0.4513 mA
I3 = -0.5638 mA What does negative current mean?
Current really flows in other direction
Now label currents through each resistor on the circuit diagram
I1
I2
I3
3.1228
0.4513
0.5638
2.6715
1.0151
3.1228
0.4513
0.5638

## Slide 35: Mesh Analysis (continued)
3.12V
Voltage Drop across each resistor is product of the current through the resistor and the resistance (Ohm’s Law V = IR)
Voltage drop across 1 kW resistor?
3.1228
0.4513
0.5638
2.6715
1.0151
+
+
+
+
+
+
+
-
-
-
-
-
-
-
3.35V
2.53V
2.65V
5.88V
Voltage drop across 2.2 kW resistor?
3.1228
0.4513
0.5638
2.6715 mA * 2.2 kW = 5.88 V
3.1228 mA * 1 kW = 3.1228 V

## Slide 36: Mesh Analysis (continued)
3.12V
Is there a way to check these results?
Use Kirchoff’s Voltage Law around each loop:
Loop 1: 9V – 3.12V – 5.88V = 0 V
Loop 2: 5.88V - 2.53V – 3.35V = 0 V
Loop 3: 3.35V + 2.65V – 6V = 0 V
Note: Loop voltages may not exactly equal to zero due to round-off errors.
3.1228
0.4513
0.5638
2.6715
1.0151
+
+
+
+
+
+
+
-
-
-
-
-
-
-
3.35V
2.53V
2.65V
5.88V