## Slide 1: Bits, Bytes, & Data Types

## Slide 2: Why does it matter how data is stored on a computer?
Example: Perform each of the following calculations in
your head.
a = 4/3
b = a – 1
c = 3*b
e = 1 – c
What does MATLAB get?

## Slide 3: Why does it matter how data is stored on a computer?
What does MATLAB get?
a = 4/3 = 1.3333
b = a – 1 = 0.3333
c = 3*b = 1.0000
e = 1 – c = 2.2204e-016

## Slide 4: What is going on?
Computers store all data (numbers, letters, instructions, …) as strings of 1s and 0s (bits).
A bit is short for binary digit. It has only two possible
values: On (1) or Off (0).
It is simply not possible to perfectly represent all real numbers using a finite string of 1s and 0s.

## Slide 5: Terminology
A bit is short for binary digit. It has only two possible
values: On (1) or Off (0).
A byte is simply a string of 8 bits.
A kilobyte (kB) is 1000 bytes
A megabyte (MB) is 1,000,000 bytes
A gigabyte (GB) is 1,000,000,000 bytes
For a sense of size, click on link below:
http://highscalability.com/blog/2012/9/11/how-big-is-a-petabyte-exabyte-zettabyte-or-a-yottabyte.html

## Slide 6: Binary Number System
The binary number system is a base 2 number system
(0 or 1). It is based on powers of 2.
The decimal number system is a base 10 number system
(0, 1, 2, … 9). It is based on powers of 10.
What does 5312 mean in a base 10 system?
1000 | 100 | 10 | 1
103 | 102 | 101 | 100
5 3 1 2 = 5*10^3 + 3*10^2 + 1*10^1 + 2*10^0

## Slide 7: Binary Number System
So what do the following binary numbers translate to in
a decimal system?
0 0 1 0 0 0 1 1
1 0 0 1 0 0 0 1
1 0 1 0 1 0 1 0
1*2^5 + 1*2^1 + 1*2^0 = 35
1*2^7 + 1*2^4 + 1*2^0 = 145
1*128 + 1*32 + 1*8 + 1*2 = 170
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 8: Exercise 1
Convert the following decimal numbers to binary.
6
19
47

## Slide 9: Exercise 1: Answers
6 = 1 1 0 1*2^2 + 1*2^1 + 0*2^0
19 = 1 0 0 1 1 1*2^4 + 1*2^1 + 1*2^0
47 = 1 0 1 1 1 1 1*2^5 + 1*2^3 + 1*2^2 +
1*2^1 + 1*2^0

## Slide 10: MATLAB Functions for Conversion
bin2dec(‘ ‘)
converts a string of bits to a decimal number
dec2bin( )
converts a decimal number into a string of bits

## Slide 11: Exercise 2
Try to work out some systematic method of converting a
decimal number to a binary string without using a
software program to do it for you.
Suggestion: work with a relatively large number like 181

## Slide 12: Subtraction Method
Find the largest power of 2 that doesn’t exceed the number.
Subtract the power of 2 from the original number and put a 1 down for this power of 2.
Keep repeating steps 1 and 2 for each result from the subtraction operation.

## Slide 13: Subtraction Method
Example: Convert 181 to binary
128 is the largest power of 2 that doesn’t exceed 181. Put a 1 in the 128 place and 181-128 = 53
32 is the largest power of 2 that doesn’t exceed 53. Put a 1 in the 32 place and 53 – 32 = 21. Also, put a 0 in for 64 since it didn’t fit within 53.
16 is the largest power of 2 that doesn’t exceed 21. Put a 1 in the 16 place and 21 – 16 = 5.
Continue the procedure to get the bit pattern shown below:
1 0 1 1 0 1 0 1
128 64 32 16 8 4 2 1 181 = 1 0 1 1 0 1 0 1

## Slide 14: Divide by 2 Method
Example: Convert 181 to binary
181/2 = 90 r = 1 (LSB)
90/2 = 45 r = 0
45/2 = 22 r = 1 181 = 10110101
22/2 = 11 r = 0 Quit dividing when you
11/2 = 5 r = 1 get to zero.
5/2 = 2 r = 1 Remember to read bits
2/2 = 1 r = 0 from bottom to top.
1/2 = 0 r = 1 (MSB)

## Slide 15: Range of Binary System
What is the biggest number you can make with 8 bits?
What is the smallest number you can make with 8 bits?
What is the biggest number you can make with 16 bits?
11111111 = 128 + 64 + 32 +16 + 8 + 4 + 2 + 1 = 255 = 2^8 – 1
00000000 = 0
1111111111111111 = 2^16 – 1 = 65535

## Slide 16: Numeric Data Types
Data type refers to the way in which a number is represented (stored) in computer memory as a string of ones and zeros.
Name | Description | Range
double | 64 bit floating point | -1.79769313486232E308 to -4.94065645841247E-324 4.94065645841247E-324 to 1.79769313486232E308
single | 32 bit floating point | -3.402823E38 to -1.401298E-45 1.401298E-45 to 3.402823E38
uint8 | 8 bit unsigned integer | Integers from 0 to 255
int8 | 8 bit signed integer | Integers from -128 to 127
uint16 | 16 bit unsigned integer | Integers from 0 to 65535
int16 | 16 bit signed integer | Integers from -32768 to 32767
uint32 | 32 bit unsigned integer | Integers from 0 to 4294967295
int32 | 32 bit signed integer | Integers from -2147483648 to 2147483647

## Slide 17: What are some limitations of Unsigned Integers?
Limited range: 8 bits allows us to work with numbers up to 255
No negative numbers
No decimal numbers – all numbers are integers

## Slide 18: Example
In MATLAB, all numbers are stored as 64 bit doubles unless you specify another number type.
Try this:
>> a = 13; b = uint8(13);
>> 1.5*a
>> 1.5*b
Results? Why?
Now type >> whos

## Slide 19: Exercise 3
Try the following commands in MATLAB and see if you can explain the output.
uint8(16.5)
uint8(16.2)
uint8(-47)
uint8(436)
uint16(436)
uint16(1000000)
uint32(1000000)

## Slide 20: Exercise 3: Answers
uint8(16.5) = 17
uint8(16.2) = 16
uint8(-47) = 0
uint8(436) = 255
uint16(436) = 436
uint16(1000000) = 65535
uint32(1000000) = 1000000
If you exceed the range of your number system, you don’t get an error. Your numbers just get changed to fit the system.

## Slide 21: So how do we get Negative Numbers?
Use the first bit or the MSB (most significant bit) to
represent the sign of the number.
1 = negative and 0 = positive
What would happen to our range?
The range would be cut in half!
General Range Formula: -2(N – 1) to +2(N – 1) - 1
N = number of bits

## Slide 22: Numeric Data Types
Data type refers to the way in which a number is represented (stored) in computer memory as a string of ones and zeros.
Name | Description | Range
double | 64 bit floating point | -1.79769313486232E308 to -4.94065645841247E-324 4.94065645841247E-324 to 1.79769313486232E308
single | 32 bit floating point | -3.402823E38 to -1.401298E-45 1.401298E-45 to 3.402823E38
uint8 | 8 bit unsigned integer | Integers from 0 to 255
int8 | 8 bit signed integer | Integers from -128 to 127
uint16 | 16 bit unsigned integer | Integers from 0 to 65535
int16 | 16 bit signed integer | Integers from -32768 to 32767
uint32 | 32 bit unsigned integer | Integers from 0 to 4294967295
int32 | 32 bit signed integer | Integers from -2147483648 to 2147483647

## Slide 23: Exercise 4
Try to predict what the outcomes of the following
commands in MATLAB will be then check your predictions
using MATLAB.
int8(16.5)
int8(-47)
int8(-143)
int8(436)
int16(436)
a = int8(60); 5*a
5*double(a)

## Slide 24: Exercise 4: Answers
int8(16.5) = 17
int8(-47) = -47
int8(-143) = -128
int8(436) = 127
int16(436) = 436
a = int8(60); 5*a = 127
5*double(a) = 300
Same Lesson: If you exceed the range of your number system, you don’t get an error. Your numbers just get changed to fit the system.

## Slide 25: So How do we get Decimal Numbers?
Terminology:
Integer systems are also often called fixed point
systems
Decimal systems are often called floating point
systems. Floating point is somewhat similar to
scientific notation except it uses powers of 2 and the
number in front of the decimal point is always a 1.

## Slide 26: Floating Point Format: Double
A double uses 64 bits to store a number.
Conversion Formula: (-1)s⋅(1 + f)⋅2(e – 1023)
First bit (MSB) is sign bit, s. s = 0 for positive
s = 1 for negative
Next 11 bits are exponent, e. Straight unsigned binary.
Next 52 bits are fractions (negative powers of 2), f.
1/2 1/4 1/8 1/16 … 1/(2^52)

## Slide 27: Floating Point Format: Double
Example:
1 10000000010 11010 ….. 0
Conversion Formula: (-1)s⋅(1 + f)⋅2(e – 1023)
>> e = bin2dec(‘10000000010’) = 1026
-14.5
s
Sign bit
e
11 exponent bits
f
52 mantissa bits

## Slide 28: Floating Point Format: Double
Example:
0 01111101011 010010 ….. 0
Conversion Formula: (-1)s⋅(1 + f)⋅2(e – 1023)
>> e = bin2dec(‘01111101011’) = 1003
s
Sign bit
e
11 exponent bits
f
52 mantissa bits

## Slide 29: Floating Point Format: Double
1. Very large range:
-1.79769313486232E308 to -4.94065645841247E-324
4.94065645841247E-324 to 1.79769313486232E308
2. Ability to work with decimal numbers
3. What types of numbers can be represented
exactly as doubles?
  All positive and negative integers within the range
  All numbers that are powers of 2 or combinations of powers of 2.
Ex: 0.75 = ½ + ¼

## Slide 30: Additional Comments on Floating Point Numbers
Not all numbers can be represented exactly even using 64 bit floating point. We saw this in the very first example! If we do many, many calculations with numbers which are just a tiny bit off, that error can grow very, very large depending on the type of computations being performed.
64 bit doubles have a huge, but still limited range. What happens if we exceed it? Try the following:
>> a = 373^1500
>> b = factorial(172)

## Slide 31: Data Types
Choice of data type affects memory storage requirements, precision (accuracy) of computations, and dynamic range.
One example of a practical application where unsigned integers are the preferred data type is Digital Imaging (jpeg, giff, bitmap files).
MATLAB® defaults to the data type double which will be used most often in this course.
A string is an example of a non-numeric data type and is simply a list of characters.

## Slide 32: Hexadecimal Systems
A hexadecimal system is a base 16 system (0-9, A, B, C, D, E, F) which is a useful shorthand system for binary (strings of 1s and 0s can get long and difficult to read or write).
A = 10
B = 11
C = 12
D = 13
E = 14
F = 15

## Slide 33: Converting between Binary and Hex
Binary to Hex: Put bits in groups of 4 starting from right (LSB)
then change each group to Hex value
Example: 1100000110011111
1100 0001 1001 1111
12 = C 1 9 15 = F
Answer: C19F

## Slide 34: Converting between Binary and Hex
Hex to Binary: Replace each Hex digit with a 4 bit binary code
Example: D15A
D=13 1 5 A=10
1101 0001 0101 1010
Answer: 1101000101011010

## Slide 35: ASCII Code
When you press a key on your computer keyboard, the key that you press is translated to a binary code.
A = 1000001 (Decimal = 65; Hex 41)
a = 1100001 (Decimal = 97; Hex 61)
0 = 0110000 (Decimal = 48; Hex 30)

## Slide 36: ASCII Code

## Slide 37: ASCII Code
Example: If you were typing a word document, the
word:
Hello
In Dec would translate to: 72 101 108 108 111
In Hex would translate to: 48 65 6C 6C 6F
Of course, it is actually stored in binary but a big long
string of 1s and 0s is pretty hard to read!

## Slide 38: Exercise 5: Intro to Strings
Do the following in MATLAB:
>> my_name = 'insert your name between single italics‘
>> my_name(1)
>> my_name(2)
>> my_name(100)
>> double(my_name)
>> 2*my_name
>> char([72 69 76 76 79])