## Slide 1: Interpolation

## Slide 2: Interpolation
Interpolation is the process of inserting data points in between existing data points.

## Slide 3: Warm-up Problems
Viscosity is a measure of a fluid’s resistance to flow. Using nearest point interpolation, estimate the viscosity of water at a temperature of 18oC.
Temperature (oC) | Dynamic Viscosity (cP) of Water
10 | 1.307
20 | 1.002
30 | 0.797
40 | 0.653
50 | 0.532
60 | 0.467
1 cP (centipoise) = 0.001 N-s/m2

## Slide 4: Warm-up Problems
Temperature (oC) | Dynamic Viscosity (cP) of Water
10 | 1.307
20 | 1.002
30 | 0.797
40 | 0.653
50 | 0.532
60 | 0.467
Using linear interpolation, estimate the viscosity of water at a temperature of 18oC.

## Slide 5: Types of Interpolation
Nearest point – round to the nearest existing data point.
Linear – insert values along a straight line between two adjacent data points.
Polynomial Interpolation – insert values along a polynomial that perfectly fits N adjacent data points. Note: The polynomial will be order N – 1 or lower.
Spline Interpolation – creates a set of lower order polynomials between adjacent data points that fit together with the polynomials in adjacent intervals. (MATLAB uses cubic spline).
Many, many other algorithms including filtering.

## Slide 6: MATLAB function: interp1
yint = interp1(x,y,xint,method)
The function, interp1, uses the original x and y values (data points) and interpolates to find the new values yint at the desired points in xint.
Methods: ‘nearest’ ‘linear’ ‘spline’ or ‘pchip’
Original x, y
Desired x
Desired y

## Slide 7: Apply interp1 to Warm Up Problem
>> interp1([10 20],[1.307 1.002],18,'linear')
ans =
1.0630
What if we wanted to calculate the viscosity at temperatures of 12, 14, 16, and 18?
>> interp1([10 20],[1.307 1.002],12:2:18,'linear')
ans =
1.2460 1.1850 1.1240 1.0630

## Slide 8: Apply interp1 to Spring-Mass Data
Time (s) | Displacement (cm)
0 | 1
0.5 | 0
1 | -0.61
1.5 | 0
2 | 0.37
2.5 | 0
3 | -0.22
3.5 | 0
4 | 0.14
4.5 | 0
5 | -0.08
We want to estimate the displacement of the mass every 0.1 seconds using the measured sensor data. The measured data can be entered in by hand or imported using the Excel file named MassSpringDisplacementData.

## Slide 9: Nearest Point Interpolation
% Enter Original Data Points or import excel from file!
>> t = 0:0.5:5;
>> d = [1 0 -0.61 0 0.37 0 -0.22 0 0.14 0 -0.08];
% Enter Desired Time Values
>> t_int = 0:0.1:5;
% Use interp1 to get estimates for displacement
>> d_int_nearest = interp1(t,d,t_int,'nearest');
>> plot(t_int,d_int_nearest,'ko',t,d,'r*')

## Slide 10: Nearest Point Interpolation

## Slide 11: Linear Interpolation
% Original Data Points
>> t = 0:0.5:5;
>> d = [1 0 -0.61 0 0.37 0 -0.22 0 0.14 0 -0.08];
% Enter Desired Time Values
>> t_int = 0:0.1:5;
% Use interp1 to get estimates for displacement
>> d_int_linear = interp1(t,d,t_int,‘linear');
>> plot(t_int,d_int_linear,'ko--',t,d,'r*')

## Slide 12: Linear Interpolation

## Slide 13: Spline Interpolation
% Original Data Points
>> t = 0:0.5:5;
>> d = [1 0 -0.61 0 0.37 0 -0.22 0 0.14 0 -0.08];
% Enter Desired Time Values
>> t_int = 0:0.1:5;
% Use interp1 to get estimates for displacement
>> d_int_spline = interp1(t,d,t_int,'spline');
>> plot(t_int,d_int_spline,'ko--',t,d,'r*')

## Slide 14: Linear Interpolation

## Slide 15: Interpolation
Notice that interpolation doesn’t change the original data points – it simply stuffs new points in between the original data points!
Which method seems best for the spring-mass example? Why?

## Slide 16: Interpolation
There is a trade-off between accuracy and complexity of calculations.
Polynomial and spline require more adjacent data points, are more computationally intensive than linear or nearest, and introduce a larger time delay for real-time applications.
However, polynomial and spline tend to produce more accurate values (unless of course, the data truly is linear).

## Slide 17: Interpolation vs. Curve Fitting
Interpolation stuffs new data points between existing points without attempting to determine some overall mathematical expression. Interpolation utilizes equations that are satisfied by the subset of existing data points being used for the interpolation calculation. Existing data points are not modified.
Curve fitting does not require that any of the existing data points satisfy the resulting mathematical expression. It is possible that none of the original data points are on the graph of the resulting function.

## Slide 18: Interpolation vs. Curve Fitting
Note: Polynomials are not good functions for describing damped oscillations. We will look at a much better equation for damped oscillations later on.

## Slide 19: Demo Audio Compression/Interpolations
Compressed_Audio.m
Hear and see the effect of compression on a 1000 Hz tone.
Interpolation_Audio.m
Hear and see the effect of different types of interpolation on a 1000 Hz tone.